## Slide 1: RQT Graph

## Slide 2: ROS Nodes Layout

## Slide 3
Waypoint Files Summary
filename | Column headers | Notes
churchlot_with_cars.csv | Pos x,y,z, yaw(rad) | Yaw is in rad (+/- Pi)
sim_waypoints.csv | Pos x,y,z, yaw(?) | Yaw is constant – bad? Same path as wpt_yaw and wpt_yaw_const
wp_yaw.txt | Pos x,y,z, yaw(deg) | Identical to wp_yaw_const.txt
wp_yaw_const.txt | Pos x,y,z, yaw(deg) | Identical to wp_yaw.txt Yaw is in deg(0-360)

## Slide 4: churchlot_with_cars.csv
Total Waypoints: 61
Distance Traveled Over Entire Waypoint Path: 68.4871
Column Headers: Pos x,Pos y, Pos z, yaw(rad)
Yaw goes from +/- pi (rad)
1 unit of distance traveled
between waypoints

## Slide 5: sim_waypoints.csv
Distance between waypoints
not constant, speed changing
Yaw angle bad?
Total Waypoints: 11011
Distance Traveled Over Entire Waypoint Path: 7014.1148
Column Headers: Pos x,Pos y, Pos z, yaw(rad)
Yaw is constant, doesn’t make sense

## Slide 6: wpt_yaw_const.txt
Distance between waypoints
not constant, speed changing
Total Waypoints: 10902
Distance Traveled Over Entire Waypoint Path: 6968.739
Column Headers: Pos x,Pos y, Pos z, yaw(deg)
Yaw goes from 0 to 360 deg
Same path as sim_waypoints.csv, but yaw is correct in this file

## Slide 7: wpt_yaw.txt
Distance between waypoints
not constant, speed changing
Total Waypoints: 10902
Distance Traveled Over Entire Waypoint Path: 6968.739
Column Headers: Pos x,Pos y, Pos z, yaw(deg)
Yaw goes from 0 to 360 deg
Same path as sim_waypoints.csv, but yaw is correct in this file

## Slide 8
waypoint_loader.py
0.27778 is km/hr to m/s conversion
3.6 is m/s to km/hr conversion
Output waypoints are in /world frame
Target speed set in launch file (in km/hr)

## Slide 9
waypoint_updater.py
Hardcoded number of waypoints to publish (200)
Publishing more that 20 waypoints ahead causes simulator to lag

## Slide 10
waypoint_follower
AKA pure_pursuit node
Not clear if this requires changes at this time
Produces estimated angular rate based on curvature of road, need to combine this with CTE control for steering control

## Slide 11
twist_controller: launch files
3 launch files:
dbw.launch – runs dbw_node.py and sets params below
dbw_test.launch – loads rosbag dbw_test.rosbag.bag
Assigns topics from rosbag:
/vehicle/throttle_cmd =/actual/throttle_cmd
/vehicle/steering_cmd =/actual/steering_cmd
/vehicle/brake_cmd =/actual/brake_cmd
dbw_sim.launch - runs dbw_node.py and sets params below
Units?
param name="vehicle_mass" value="1736.35"
param name="fuel_capacity" value="13.5"
param name="brake_deadband" value="0.1"
param name="decel_limit" value="-5.0"
param name="accel_limit" value="1.0"
param name="wheel_radius" value="0.2413"
param name="wheel_base" value="2.8498"
param name="steer_ratio" value="14.8"
param name="max_lat_accel" value="3.0"
param name="max_steer_angle" value="8.0"

## Slide 12
twist_controller: dbw_node.py
This node calls the throttle, steering and brake controllers, it publishes the commands to the car/simulator.
Car model parameters are provided for use in the control design.

## Slide 13
twist_controller: low_pass.py
Simple Low Pass Filter:
tau =0, ts = 1 will shut off this filter

## Slide 14
twist_controller: pid.py
Kp
Ki
Kd
Error
+
prev
-
1/Ts
1/Ts
+
INPUT
OUTPUT
Limit